IMPELLER FAN DIMENSIONS

A= 820.74mm

B=180mm

C=110mm

D=25mm

E=579.24mm

M=120.9mm

IMPELLER FAN CONSTRUCTION MATERIAL  GUAGE

Rear Plate Thickness   is 4mm

Impeller Blade thickness is 6mm

Impeller conelike end Plate is 3mm

Hub diameter is 120.90mm (must be able to accommodates 60mm shaft diameter)

Number of Blades is 12

INLET CONE DIMENSIONS

F=560mm

G=260mm

H=1,040.7mm

I=bolt to bolt centre distance = 195mm

J=Number Of holes for bolt is 16

K=Distance from holes to the edge is 20mm

L=Holes diameter is 15mm

Please note that these impellers Fans are driven by a single electric motor with 2 shafts one impeller at the right hand and another at the left hand and they sucks air from the Radiator fins in opposite direction, this must be noted during construction / Fabrication

In Event of any other query do not hesitate to contact us immediately