DATA SHEET

Three-phase Induction Motor - Squirrel Cage

Product code:

Product line: Standard Efficiency

Frame: 225S/M

Output: 37 kW

Frequency: 50 Hz

Poles: 4

Rated speed: 1470-1475-1475 rpm

Slip: 2.00-1.67-1.67 %

Rated voltage: 380-400-415/660-690V

Rated current: 70.2-67.4-67.4/40.4-39.1 A

L. R. Amperes: 470-452-452/271-262 A

Il/In: 6.7

No load current: 28.0-31.0-37.0/16.1-18.0 A

Rated torque: 24.5-24.4-24.4 kgfm

Locked rotor torque: 210-230-240 %

Breakdown torque: 240-280-300 %

Design: N

Insulation class: F

Locked rotor time: 17-17-17 s (hot)

Service factor: 1.00

Duty cycle: S1

Ambient temperature: -20°C to +40°C

Altitude: 1000 m.a.s.l

Enclosure: IP55 (TEFC)

Mounting: B3T

Rotation: Both

Aprox. Weight*: 334 kg

Moment of inertia: 0.55990 kgm²

Sound Pressure Level: 70.0 dB (A)

Front Rear Load Power factor Efficiency (%)**

Bearing 6314-C3 6314-C3

Regreasing int. 11638 h 11638 h

Grease amount 27 g 27 g

Grease - Polyrex EM - ESSO

100% 0.87-0.86-0.83 92.1-92.2-92.0

75% 0.83-0.81-0.77 91.8-91.7-91.5

50% 0.75-0.71-0.67 91.0-90.6-90.0

Notes:

The figures given herewith are regarded as guaranteed values and applied to sinusoidal power supplied motors, within permissible

Tolerances under IEC 60034-1. Noise level with tolerance of +3 dB(A).